## Slide 1
Lenovo Remote Workstation (TGX Sender)
ThinkStation P Series Tower/Rack Workstation
  CPU: Intel Corei or Xeon Class
  Memory: 8GB+
  Graphics: NVIDIA Quadro P1000 or greater (latest driver)
  Storage: Solid State Drive
  OS: MS Windows 10 or Linux (CentOS/RHEL 7, Ubuntu 18.04) or above
Note: Sender/Host Workstation specifications need to match the typical hardware requirements of the associated ISV certified applications (CPU, Memory, Storage, Graphics etc)
Minimum Hardware Requirements - TGX Remote Workstation
Lenovo Remote Workstation (TGX Receiver)
ThinkStation or ThinkPad P Series Workstations
  CPU: Intel Core i or Xeon Class
  Memory: 8GB+
  Graphics: Integrated Intel HD Video (CPU Graphics) Recommended NVIDIA Quadro P620 or above (latest driver)
  Storage: Solid State Drive
  OS: MS Windows 10 or Linux (CentOS/RHEL 7, Ubuntu 18.04) or above
Note: TGX can leverage NVIDIA and Intel hardware optimized decoders; however the use of NVIDIA Quadro GPUs is recommended for maximum performance, lowest latency & multiple 4k monitors. Competitor MacOSX, Windows & Linux client devices can be supported providing the above basic hardware requirements are met. Limitations apply.
TGX Caveats/Gotchas
Although TGX version 1.10.7 can support both NVIDIA GeForce & NVIDIA Quadro GPUs, performance and features are restricted on consumer GeForce GPUs. Note: This is due to the limited number of NVENC chips + maximum number of concurrent sessions. Detailed NVIDIA GPU support & feature matrix can be found here.
TGX version 1.10.7 supports a wide variety of desktop configurations with the following caveats:
Windows based Senders running NVIDIA GeForce GPUs CANNOT offer fully configurable desktop resolutions and ONLY support the remote workstation desktop ‘as is’ on the receiver – LIMITED FEATURES
Windows based Receivers can support up to 4x monitors and can request the desktop of the Sender to “Match Entire Desktop” or “Match a Single Monitor” of the Receiver – FULLY FEATURED
MacOSX & Linux Receivers can only select “Match a Single Monitor” so NO multi-monitor support. Planned future release of TGX version 2.1 will support Match Entire Desktop on all OS platforms.